 Distance and Buffers
Lecture #13 | GEOG 510
GIS & Spatial Analysis in Public Health
Varun Goel

---
Outline
- Distance
  - Euclidean distance
    - Distance to features
    - Buffer
  - Alternate distances
    - Great circle, Manhattan, Network, Cost distance (raster)

---
Distance
- Why distance?
  - Distance is a fundamental geographic concept that affects relationships and interactions among phenomena
    - Sometime we want to explain it
    - Sometimes we want to measure it for input to other calculations
    - Sometimes we want to map it

---
Euclidean Distance
- Based on Pythagorean Theorem
  - a2 + b2 = c2
  - Assumes:
    - A planar Earth (i.e., a projected cs)
    - No differences in elevation
  Euclidean distance is also called “Cartesian” distance in ESRI help
Does not require GIS!... simple mathematical calculation
size 12{d= sqrt { left (x rSub { size 8{2} } - x rSub { size 8{1} } right ) rSup { size 8{2} } + left (y rSub { size 8{2} } - y rSub { size 8{1} } right ) rSup { size 8{2} } } } {}
(x2, y2)
(x1, y1)
x
y

---
Distance: Vector
- Point distance
  - Distance between points
- Line length
  - Distance between nodes
  - Distance between vertices
    - Sum of segment lengths
- Polygon Perimeter
  - Distance between vertices
    - Sum of segment lengths

---
Distance to Features
- Measure distance from one set of features to another
  - Vector distance tool
  - Near
    - Locate nearest feature, return distance
  - Generate Near Table
    - Locate k nearest features, return distance
      - Output written to a new table

---
Distance: Raster
- Measured from some source cell
  - Or, source cells (could be a line or polygon)
  - Distance from each cell to source calculated as Euclidean distance
2.8	2.2	2	2.2	2.8
2.2	1.4	1	1.4	2.2
2	1	0	1	2
2.2	1.4	1	1.4	2.2
2.8	2.2	2	2.2	2.8
1.4	1	1.4
1	0	1
1.4	1	1.4
d

---
Distance to Features
Raster maps of distance are commonly used as measures of accessibility

---
Buffers
- A buffer is a region surrounding a feature (or set of features)
  - Region (or neighborhood) defined using a set distance from a given feature (point, line, polygon, grid cell, or group of cells)
  - Create new spatial objects defined as the area within a specified distance from existing features

---
Buffers
- A buffer is a region surrounding a feature (or set of features)
  - Region (or neighborhood) defined using a set distance from a given feature (point, line, polygon, grid cell, or group of cells)
  - Create new spatial objects defined as the area within a specified distance from existing features

---
Buffers
- A buffer is a region surrounding a feature (or set of features)
  - Region (or neighborhood) defined using a set distance from a given feature (point, line, polygon, grid cell, or group of cells)
  - Create new spatial objects defined as the area within a specified distance from existing features

---
Buffer Output
- Output shape options for overlapping buffers in same feature class
  - An autonomous buffer for each feature
    - Retains input features' attributes
1
2
3
Planar topology?
1
2
3

---
Buffer Output
- Output shape options for overlapping buffers in same feature class
  - An autonomous buffer for each feature
    - Retains input features' attributes
  - Dissolved output
    - Original features' attributes cannot be “separated”
1
2
3

---
Interior Buffer
- Interior polygon buffers
  - Rather than choose a distance “outside” of the polygon, an interior buffer (“setback”) can be created
    - Use a “negative” value for the buffer distance

---
Variable Distance Buffer
- Buffer distance can be the same for all objects in a feature class (fixed-distance)
  - Buffer distance can also vary
    - Variable-distance buffer
    - Based on an attribute in the feature class

---
Euclidean Distance
- Limitations
  - Assumes flat earth
    - Especially limiting over large distances
  - Assumes no slope in terrain
    - Especially limiting in mountainous terrain
  - Assumes no barriers to movement
    - Barriers can include anything that’s not a road (in the case of vehicular travel) or anything on the landscape that stands in the way

---
Great Circle Distance
- Great circle distance is the shortest distance between two points on a sphere
  - Used for points stored in spherical coordinates
  - Required to calculate distance in spherical coordinates, especially if points are far apart
  Also called “geodesic” distance in ESRI help
Point 1: (λ1,Φ1) ← longitude, latitude
Point 2: (λ2,Φ2) ← longitude, latitude
R: radius of the Earth (~6378km)
D = R cdot cos^{-1}((sin %phi_{1} cdot sin %phi_{2})+(cos %phi_{1} cdot cos %phi_{2} cdot lline %lambda_{1} - %lambda_{2} rline))
D

---
Manhattan Distance
- One way to account for barriers is to recognize that travel can be limited to transportation routes that follow cardinal directions (N, S, E, W)
  - e.g., in Manhattan where most streets are at right angles
size 12{d= lline x rSub { size 8{2} } - x rSub { size 8{1} } rline + lline y rSub { size 8{2} } - y rSub { size 8{2} } rline } {}
x
(x2, y2)
(x1, y1)
y

---
Network Distance
Network distance restricts travel along existing arcs (lines)
  - e.g., on city streets
  - Distance is the sum of the lengths of arcs that make up the route

---
Minkowski Distance
- Falls between Euclidean and Manhattan distance
- Distance of a curved arc connecting two points
  where 1 < p < 2
size 12{d= sqrt { left (x rSub { size 8{2} } - x rSub { size 8{1} } right ) rSup { size 8{2} } + left (y rSub { size 8{2} } - y rSub { size 8{2} } right ) rSup { size 8{2} } } } {}
size 12{d= lline x rSub { size 8{2} } - x rSub { size 8{1} } rline + lline y rSub { size 8{2} } - y rSub { size 8{2} } rline } {}
size 12{d= nroot {p} { left (x rSub { size 8{2} } - x rSub { size 8{1} } right ) rSup { size 8{p} } + left (y rSub { size 8{2} } - y rSub { size 8{2} } right ) rSup { size 8{p} } } } {}

---
Shortest Path (Raster)
- Greater distances are in lighter shades
- Straight lines emanating from source location

---
Cost Distance
- Implemented as a modification to calculating raster distance
  - Functional or cost distance
    - User defines relative barriers to movement by mapping the cost, or friction, of movement for each raster cell
    - Cost can be defined by any spatial feature or attribute that limits the ability of people, animals, ideas, diseases, air, etc. to move across the landscape

---
Cost Distance
TOTAL COST, c = 1.4
Cost
2	1	1
2	1	1
2	1	1
destination
c = 0.7 * 1
c = 0.7 * 1
source
Distance
1.4	1	1.4
1	0	1
1.4	1	1.4

---
Calculate Cost Distance
1	1	1	1	1
1	4	1	1	1
1	4	1	1	1
1	4	1	1	1
1	1	1	1	1
- Create a grid of costs (cost grid) to define the relative cost of traversing each grid cell
- Identify source cell(s)
- Calculate “cost distance” as the sum of unit costs accumulated to get from one place to other places
- Identify least cost path
  - i.e., the path of minimum cost between places
3.4	2.4	2	2.4	2.8
3.8	3.5	1	1.4	2.4
4.8	2.5	0	1	2
3.8	3.5	1	1.4	2.4
3.4	2.4	2	2.4	2.8
Cost grid
Cost distance
(minimum to
all cells in grid)
3.4	2.4	2	2.4	2.8
3.8	3.5	1	1.4	2.4
4.8	2.5	0	1	2
3.8	3.5	1	1.4	2.4
3.4	2.4	2	2.4	2.8
0	1	0	0	0
1	0	1	0	0
0	0	1	0	0
0	0	0	0	0
0	0	0	0	0
Least cost path

---
Cost Distance Example
- Cost grid: Slope
- Slope value is relative barrier (higher is darker)
- Lake is absolute barrier
- Cost Distance and Least Cost Path
- Greater accumulated cost distance is in lighter colors

---
Cost Distance
- Catchment area (like buffer)
  - Area within a specific “cost” of source
    - e.g., cost < 3.5
3.4	2.4	2	2.4	2.8
3.8	3.5	1	1.4	2.4
4.8	2.5	0	1	2
3.8	3.5	1	1.4	2.4
3.4	2.4	2	2.4	2.8
3.4	2.4	2	2.4	2.8
3.8	3.5	1	1.4	2.4
4.8	2.5	0	1	2
3.8	3.5	1	1.4	2.4
3.4	2.4	2	2.4	2.8

---
Keywords
- Buffer
- Distance
  - Euclidean, Great circle, Manhattan, Network, Minkownski
  - Least Cost Path
    - Functional or cost distance